## Slide 1: ACL – Solution for Assignment 1
West(config)# access-list 111 deny ip 10.10.1.0 0.0.0.255 10.10.4.0 0.0.0.255
West(config)# access-list 111 permit ip 10.10.1.0 0.0.0.255 10.10.0.0 0.0.255.255
West(config)# access-list 111 permit tcp 10.10.1.0 0.0.0.255 any eq 80
West(config)# access-list 111 deny ip 10.10.1.0 0.0.0.255 any
West(config)# access-list 111 permit ip any any
West(config)# interface f0/0
West(config-if)# ip access-group 111 in

## Slide 2: ACL – Solution for Assignment 2
West(config)# ip access-list extended ONE_AND_TWO_WAY
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255 range 20 21
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255 eq 21
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255 gt 1023
West(config-ext-nacl)#deny ip 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255 eq 80
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 eq 80 10.10.3.0 0.0.0.255
West(config-ext-nacl)#deny ip 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255
West(config-ext-nacl)#permit ip any any
West(config-ext-nacl)#exit
West(config)# interface f0/1
West(config-if)# ip access-group ONE_AND_TWO_WAY in

## Slide 3: ACL – Solution for Assignment 3
Gateway(config)# ip access-list extended GATEWAY
Gateway (config-ext-nacl)# deny icmp any any echo
Gateway (config-ext-nacl)# permit tcp any 10.10.1.2 0.0.3.0 eq 80
Gateway (config-ext-nacl)# permit tcp any any established
Gateway (config-ext-nacl)# deny tcp any any
Gateway (config-ext-nacl)# permit ip any any
Gateway (config-ext-nacl)# exit
Gateway (config)# interface f0/0
Gateway (config)# ip access-group GATEWAY in